Notes 14.3 Power

Power – rate at which electrical energy is changed into other forms of energy such as heat, sound, motion or light.

- Units: Watts (W),  kilowatt(kW) = 1000 W

- A 100-W light bulb uses 100 Joules of electrical energy each second.

- Higher the wattage – more energy you use.

If a 1200-Watt blow dryer is plugged into a household circuit (assume V=120V), how much current is flowing through the        	    heating element?

In a house wired in parallel, the power used by different devices simply adds:

Total Power = P1 + P2 + P3 + …..

What is the maximum wattage that a 20-amp circuit breaker can handle if it is supplied with 120 volts?

How many 100 W light bulbs could run on the circuit?

# Text boxes

Power(watts) = current(amps) x voltage(volts)

P = IV